## Slide 1: HEX20
Onboard Telecommand Reception & Routing
Final Demonstration Package — M11

## Slide 2: Problem & Objective
Receive telecommands over a noisy uplink
Decode and validate transfer frames and Space Packets
Route by APID + PUS service/subtype
Reject corrupted, unauthenticated, replayed and inconsistent commands

## Slide 3: System Architecture
Noisy uplink → frame synchronization → CRC validation
Space Packet decoding → security gate
HMAC + freshness/replay check → APID/service/subtype binding
PUS handlers → telemetry, counters and dashboard

## Slide 4: Supported PUS Demonstration
HKR — APID 100 / ST 3,1
MEM — APID 101 / ST 6,2
FUN — APID 102 / ST 8,128
CON — APID 103 / ST 17,1

## Slide 5: Security Gate
Development/demo authenticated envelope
HMAC authentication
Monotonic freshness/replay protection
Authenticated command must match packet routing fields
Failures stop before command handler execution

## Slide 6: Validation Campaign
1,000 deterministic scenarios
680 benign/acceptance cases
320 fault or attack cases
CRC, authentication, header, malformed packet and replay tests
Noise recovery and end-to-end routing included

## Slide 7: Live Dashboard
Streamlit dashboard built around the actual end-to-end processor
Command transmission for HKR/MEM/FUN/CON
Authentication, CRC and header fault injection
Event log, counters, stage/reason and latency visibility

## Slide 8: Evidence & Traceability
M1–M10 implementation and verification artifacts
M10 JSON/CSV validation evidence
M11 requirements-to-verification matrix
Repeatable presenter checklist and demo flow

## Slide 9: Engineering Limitations
Software prototype; not flight qualified
Timing measurements are machine-dependent
Development security secret must not be reused
Production requires mission-approved cryptography, key management, exact CCSDS/PUS profile validation and hardware-in-the-loop testing

## Slide 10: Final Demonstration Flow
1. Start dashboard
2. Demonstrate valid HKR/MEM/FUN/CON
3. Trigger authentication rejection
4. Trigger CRC rejection
5. Trigger routing/header rejection
6. Show M10 1,000-command validation evidence